## Slide 1
Boolean Algebra
Lecture 5 · functions, forms & minimization
Canonical forms · Karnaugh maps · Quine–McCluskey · gates · completeness
Notes: From a truth table to the SMALLEST circuit. Today: how many functions there are, functional completeness, canonical forms, and the two minimisation methods — Karnaugh maps and Quine–McCluskey.

## Slide 2
From tables to minimal circuits
We have
A function, given by its truth table.
We want
The cheapest expression / circuit computing it.
Two tools
Karnaugh maps (by eye) and Quine–McCluskey (by algorithm).
Notes: Every truth table can be built as a circuit — but naively that circuit is huge. Minimisation finds a small equivalent, saving gates, power, and delay.

## Slide 3
The 16 functions of two variables
2^(2²) = 16
Every 2-input function is one of sixteen.
The familiar ones: AND, OR, XOR, NAND, NOR, XNOR.
NAND and NOR turn out to be special.
Notes: With four input rows and a free output bit each, there are exactly 16 two-variable functions. Most are named; NAND and NOR are the ones from which all others can be built.

## Slide 4
Functional completeness
A basis builds everything
{¬, ∧, ∨} is complete — every function is expressible.
So is {¬, ∧} and {¬, ∨} (via De Morgan).
But {∧, ∨} alone is NOT — with no ¬ you cannot invert.
Question: can a SINGLE operator suffice?
{¬, ∧, ∨}
expresses every Boolean function
Notes: A set of operators is functionally complete if every Boolean function can be written using only them. The standard basis is {¬,∧,∨}; De Morgan lets us drop one of ∧/∨, but negation is indispensable — {∧,∨} alone builds only monotone functions. Shannon's expansion, f = x·f(x=1) ∨ x̅·f(x=0), constructively shows why {¬,∧,∨} suffices: it splits any function on one variable and recurses.

## Slide 5
One gate rules them all: NAND
NAND (and NOR) are universal
¬p = p ↑ p
p ∧ q = (p ↑ q) ↑ (p ↑ q)
p ∨ q = (p ↑ p) ↑ (q ↑ q)
So a chip can be ALL NAND gates.
Notes: Remarkably, the single operator NAND (or NOR) is complete on its own. Manufacturers exploit this: a fabric of identical NAND gates can realise any logic, simplifying design and production.

## Slide 6
Logic gates
Symbols for the connectives
Each connective is a standard gate symbol.
A bubble on the output means negation (NAND, NOR).
Wires carry single bits between gates.
Notes: These IEEE gate symbols are the vocabulary of circuit diagrams. The little bubble is inversion — an AND with a bubble is a NAND.

## Slide 7
From expression to circuit
Read the formula as wiring
Each operator becomes a gate; each variable a wire.
Inner operations feed outer ones.
f = (a ∧ b) ∨ c → an AND into an OR.
Notes: Translating a Boolean expression to hardware is mechanical: build the parse tree of the formula and replace each node with its gate. Minimising the formula first means fewer gates.

## Slide 8
A real circuit: the half-adder
Add two bits
Sum S = a ⊕ b — 1 when the bits differ.
Carry C = a ∧ b — 1 only when both are 1.
Two gates add one bit: the atom of arithmetic.
Notes: The half-adder is the smallest arithmetic circuit: XOR produces the sum bit and AND the carry. Chaining full-adders — which also accept a carry-in — builds the ripple-carry adder inside every ALU. This is Boolean algebra literally performing addition, and it shows why the connectives of Lecture 4 are the foundation of computer arithmetic.

## Slide 9
Minterms & maxterms
Name each row
Minterm: the AND of all variables making one row true.
Maxterm: the OR making one row false.
A function = the rows where it is 1.
Notes: Each row of the truth table has a minterm (a product true only there) and a maxterm. Listing the rows where f=1 gives its minterms — the raw material for canonical forms.

## Slide 10
Canonical DNF — SOP (sum of products)
f = ⋁ (minterms where f=1)
OR together the minterm for every 1-row.
f is 1 on rows 1,3,5,6,7 — five minterms:
f = a̅b̅c ∨ a̅bc ∨ ab̅c ∨ abc̅ ∨ abc.
Correct, but rarely minimal.
Notes: The canonical disjunctive normal form ORs one product per 1-row. Here f equals 1 on rows 1, 3, 5, 6, and 7, so five minterms are ORed together. It always works and is unique, but it uses the maximum number of literals — the Karnaugh map will shrink it to F = ab ∨ c.

## Slide 11
Canonical CNF — POS (product of sums)
f = ⋀ (maxterms where f=0)
AND together the maxterm for every 0-row.
The dual of SOP — group the zeros instead.
Choose whichever is cheaper for your function.
SOP ⋁∧
POS ⋀∨
Notes: POS is the dual canonical form, built from the 0-rows. SOP suits functions with few 1s; POS suits functions with few 0s.

## Slide 12
A third form: ANF (Zhegalkin)
XOR instead of OR
Every function has a UNIQUE algebraic normal form: a XOR of distinct AND-terms (plus maybe 1).
Works because {∧, ⊕, 1} is functionally complete.
The natural form for parity and checksums.
How to get it
Rewrite a̅ = a ⊕ 1 and x∨y = x ⊕ y ⊕ xy, expand, then simplify with a ⊕ a = 0 and aa = a.
Degree ≤ 1 ⇒ the function is affine (linear).
Notes: Beyond DNF and CNF there is a third, XOR-based canonical form. Since the set {AND, XOR, 1} is functionally complete, every Boolean function has a unique algebraic normal form — a XOR of distinct AND-terms, optionally including the constant 1 — called its Zhegalkin polynomial. You reach it by substituting NOT-a = a XOR 1 and OR expressed through XOR, expanding, and simplifying with a XOR a = 0 and a AND a = a. It is the natural language of parity and checksums, and a function is affine, or linear, exactly when its ANF has degree at most one.

## Slide 13
Algebraic minimization
Apply the laws
Use complement (x ∨ x̅ = 1), absorption, distributivity.
ab ∨ ab̅ = a(b ∨ b̅) = a.
Powerful, but easy to miss simplifications.
a b̅ c ∨ a b c
= a c (b̅ ∨ b)
= a c
Notes: Minimising by the laws is fully general but unsystematic — you can always find one more step, or miss one. Karnaugh maps make the adjacencies visual instead.

## Slide 14
Karnaugh maps — the idea
Adjacency = simplification
Lay the truth table on a grid where neighbours differ in one bit.
Adjacent 1s combine and drop that variable.
Rows/columns are in Gray-code order.
Notes: A Karnaugh map arranges minterms so that physically adjacent cells differ in exactly one variable. Then a block of adjacent 1s is a single product term — minimisation becomes 'draw the biggest rectangles'.

## Slide 15
Grouping the 1s
Bigger groups, fewer literals
Group 1s into rectangles of size 1, 2, 4, 8…
Each group of 2ᵏ cells removes k variables.
Cover every 1 with as few, as large groups as possible.
RED → c NAVY → ab
⇒ F = ab ∨ c
Notes: The rules: groups must be powers of two, as large as possible, and together cover all the 1s. Each doubling of a group eliminates one more variable. Here the c-block (red, four cells) and the ab-block (navy, two cells) cover all five 1s, giving the minimal F = ab ∨ c — down from five product terms.

## Slide 16
Four variables & wrap-around
16 cells, edges wrap
A 4×4 map handles four variables.
The map is a torus — left/right and top/bottom edges are adjacent.
Corners can form a single group.
Notes: Four-variable maps add wrap-around adjacency: the grid is really a torus, so opposite edges — and all four corners — are neighbours and may group together.

## Slide 17
Don't-care conditions
X = free choice
Some input combinations never occur (or the output is unused).
Mark them X and treat as 0 OR 1 — whichever enlarges a group.
Don't-cares often shrink the circuit dramatically.
Notes: Don't-cares are gifts: you may set each to 0 or 1 to make groups bigger. Exploiting them is one of the biggest real-world savings in logic design.

## Slide 18
The Quine–McCluskey algorithm
Minimisation you can program
Karnaugh maps stop working past ~5 variables.
Q–M groups minterms by their number of 1s, then merges.
Prime implicant: a group that can't grow — essential ones must be chosen.
Systematic, exact, and automatable.
Notes: Quine–McCluskey is the tabular, algorithmic version of the K-map, suitable for a computer and any number of variables. It finds prime implicants, then selects a minimal cover.

## Slide 19
Cost: before vs after
Canonical SOP
6 gates
After F = ab ∨ c
2 gates
Notes: Minimisation is not cosmetic: fewer literals mean fewer gates, less silicon area, lower power, and shorter propagation delay. The same function, a third of the hardware.

## Slide 20
Common mistakes
Groups must be 2ᵏ
Sizes 1,2,4,8… only — never a group of 3.
Use the wrap-around
Edges and corners of a K-map are adjacent.
Cover every 1
Overlap is fine; leaving a 1 uncovered is wrong.
Don't-cares are optional
Set each to 0 or 1 — only if it helps.
Notes: The classic K-map slips: illegal group sizes, forgetting wrap-around adjacency, leaving a 1 uncovered, and mishandling don't-cares.

## Slide 21
Summary
— There are 2^(2ⁿ) Boolean functions of n variables.
— {¬,∧,∨} is complete; NAND (or NOR) alone is universal.
— Canonical SOP/POS build any function from its rows.
— Karnaugh maps minimise by grouping adjacent cells.
— Quine–McCluskey does the same, algorithmically.
— Minimisation saves real gates, power, and delay.

## Slide 22
Next → Lecture 6: Propositional logic
Same connectives — now used to REASON.
Arguments, validity, satisfiability (SAT), entailment, CNF/DNF — deciding when a conclusion truly follows.
Notes: We've used ∧,∨,¬ to compute. Next we use them to REASON: when does a conclusion follow from premises? That's propositional logic — validity, entailment, and the satisfiability problem.